## Slide 1: The History of DRAM Technology
Xixi Chen
2020-04-11

## Slide 2: What's DRAM?
DRAM: usually means DDR SDRAM
  Double Data Rate
    DDR: the other technology may use SDR or QDR.
  Synchronous
    I/O and control signals are synchronized with an external clock.
    The originally dram is Asynchronous.
  Dynamic
    Dram Cell is capacitor, leak all the time, should refresh periodically.
  Random Access Memory
    Access Memory by any address, no need to sequential.

## Slide 3: SDR DDR QDR
SDR DRAM uses SDR.
(LP)DDR DDR2 DDR3 DDR4 DDR5 use DDR.
GDDR5X uses DDR or QDR.

## Slide 4: DDR or QDR of GDDR5X

## Slide 5: Why DRAM not use TDR/QDR?
Triple or quadruple transfer points in a single sine wave would be possible but would require a lot more work to determine the correct timing as data would need to transfer the next bit of data not on just an easy to determine peak. its just not simple/reliable so they don't do it(remember the receiving devices decoder has to match the same timing of the sending device or it could possible read the data to late/early).

## Slide 6
Asynchronous DRAM is an older type of DRAM used in the first personal computers. It is called "asynchronous" because memory access is not synchronized with the computer system clock. Modern PCs use SDRAM(synchronized DRAM) that responds to read and write operations in synchrony with the signal of the system clock.
Why was it phased out?
  When a program issued an instruction to access data in asynchronous memory, the data would be accessible on the system bus some time later, but this time was variable and not guaranteed. This was acceptable on older systems, until they reached speeds of about 66 MHz.

## Slide 7: Asynchronous DRAM
Conventional DRAM is controlled asynchronously, requiring the system designer to manually insert wait states to meet the specifications of the device. Timing depends on the speed of the DRAM and is independent of the system bus speed. It is these timing limitations that led to the development of the SDRAM.
SDRAM is essentially a fast DRAM with a high-speed synchronous interface. I/O‘s and control signals are synchronized with an external clock, making new options available to the designer. Simplified interface circuitry, as well as high-bandwidth data throughput can be achieved using SDRAM over conventional DRAM.

## Slide 9: Dynamic
DRAM is called dynamic, because it must be refreshed all the time or it will lose the data which it is supposed to be storing.
Refreshing DRAM means reading the data from the DRAM and directly writing them back to the DRAM. DRAM is made up of millions of very small capacitors. Each of these capacitors has a transistor to let energy in and out. The capacitor slowly loses energy, and if the DRAM is not refreshed, in the end one or more of the capacitors will let so much energy out, that for example a 1 will become a 0, so data will be lost or corrupted. Almost all computers refresh their DRAM many times per second.
You can compared to Static RAM, which doesn’t need to refresh to retain the data.

## Slide 10: Random Access Memory
When Row and Column Address is fixed, the real address in dram array is confirmed.
It’s like Two-Dimension Array.

## Slide 11: Different “Dram” Types
GDDR Wide IO HBM HMC...

## Slide 12: GDDR
GPU needs massive bandwidth, not pay attention to latency.
GDDR5 comes from DDR3.

## Slide 13: Wide IO
The design of Wide IO is designed to provide high-frequency, low-power storage for mobile system single-chip (SoC). It mainly attracts smartphones and embedded systems companies.

## Slide 14: HBM
High Bandwidth Memory (HBM) is a high-performance RAM interface for 3D-stacked SDRAM from Samsung, AMD and SK Hynix. It is used in conjunction with high-performance graphics accelerators, network devices and in some supercomputers.

## Slide 15: HMC
Hybrid Memory Cube (HMC) is a high-performance RAM interface for through-silicon vias (TSV)-based stacked DRAM memory competing with the incompatible rival interface High Bandwidth Memory (HBM).

## Slide 16: LPDDR2 S2/S4/N
S2 means 2n prefetch, S4/N means 4n prefetch.
LPDDR2-S2 also uses a double data rate architecture on the DQ pins to achieve high speed operation. The double data rate architecture is essentially a 2n prefetch architecture with an interface designed to transfer two data bits per DQ every clock cycle at the I/O pins. A single read or write access for the LPDDR2-S2 effectively consists of a single 2n-bit wide, one clock cycle data transfer at the internal SDRAM core and two corresponding n-bit wide, one-half- clock-cycle data transfers at the I/O pins.
LPDDR2-S4 and LPDDR2-N also use a double data rate architecture on the DQ pins to achieve high speed operation. The double data rate architecture is essentially a 4n prefetch architecture with an interface designed to transfer two data bits per DQ every clock cycle at the I/O pins. A single read or write access for the LPDDR2-S4 and LPDDR2-N effectively consists of a single 4n-bit wide, one clock cycle data transfer at the internal SDRAM/NVM core and four corresponding n-bit wide, one-half-clock-cycle data transfers at the I/O pins.

## Slide 17: LPDDR E Series
Core Freq: 266.7MHz

## Slide 18: Commercial/Industrial/Automotive Grade
The use of such grades ensures that a device is suitable for its application, and will withstand the environmental conditions in which it is used.

## Slide 19: Dram Innovation
SDR to DDR:

## Slide 20: DDR -> DDR2

## Slide 21: DRAM Pins

## Slide 22: VDD1/VPP
Vdd1: Core Power: memory array power.
Vpp: DDR4 word line power.
  A special high-voltage supply that supplies the potential and energy for altering the state of certain nonvolatile memory arrays. On some devices, the presence of VPP also acts as a program enable signal (P).
    References:
      JESD21-C, 1/97
  For DDR4, JEDEC decided to introduce an external VRM that provides a 2.5v electrical high voltage for the word line (row access). Since the word line voltage is no longer pumped up from the DDR voltage (like it was for DDR3), the inefficiencies of pumping up the DDR voltage are gone, and instead you get power savings.

## Slide 23: Why Dram Core/IO Power are isolate?
Since large amounts of current are sourced and sunk into the SDRAM during read and write operations, switching noise can be generated which may have an adverse effect on the memory array. Separate power inputs are provided for the I/O signals and the memory array, isolating the memory cells from possible data corruption.

## Slide 24: So many power pins?
VDD1/VDD2/VDDQ...

## Slide 25: Clock Synchronous vs Source Synchronous
The SDR memory data interface is a fully synchronous design where the data is only captured on the positive clock edge.
The DDR memory data is a true source synchronous design, where the data is captured twice per clock cycle with a bidirectional data strobe.

## Slide 26: Why CK is differential?
To increase accuracy caused by clock jitter, a differential clock was added to DDR. SDR devices use the midpoint of the rising clock edge to latch data and thus are exposed to drift. DDR uses the crossing point of CK and CK#. Using the crossing point instead of the midpoint helps negate the affects of jitter and increase margins.

## Slide 27: Output Enable
OE: Output Enable. This is an additional signal that controls output to the data I/O pins. The data pins are driven by the DRAM chip if RAS and CAS are low, WE is high, and OE is low. In many applications, OE can be permanently connected low (output always enabled), but it can be useful when connecting multiple memory chips in parallel.
It’s phased out.

## Slide 28: CKE
CKE can be used to enter power down mode, which is a low power mode.
Power Down Mode:
  Idle Power Down
  Active Power Down.
If the dram is idle for a period, the controller can issue power down mode for low power.

## Slide 29: SDR CA vs DDR CA
LPDDR3: DDR CA
DDR3/DDR4/LPDDR4: SDR CA
SDR CA:
  easier to maintain good signal integrity.

## Slide 30: Why are CA pin and DQ pin seperate?
The user interface of the memory controller is split into a command bus and a separate data bus. This split allows for maximum flexibility while ensuring the highest performance during data transactions.

## Slide 31: SDR DDR IO Interface

## Slide 32: Where does DQS come from?
For higher data rate.
In a purely synchronous system, data output and capture are referenced to a common, free-running system clock. However, the maximum data rate for such a system is reached when the sum of output access time and flight time approaches the bit time (the reciprocal of the data rate). Although generating delayed clocks for early data launch and/or late data capture will allow for increased data rate, these techniques do not ac- count for the fact that the data valid window (or data eye) moves relative to any fixed clock signal, due to changes in temperature, voltage, or loading. So, to allow for even higher data rates, data strobe signals were added to DDR devices.

## Slide 33: If no DQS...
Let's imagine time of flight for all signals is 1ns.
Situation with only one clk that is transmitted by the controller:
  During write there is no problem. Data signals can be clocked to the CLK signal and everything is fine. If traces are length matched you can use timing tolerances tighter than the time of flight.
  During read there is a problem. The controller must first transmit the clock to memory, where it arrives 1 ns later. Then the memory sends data bits to the controller and this takes another nanosecond. There is 2 ns skew, which limits how fast you can transmit.

## Slide 34: Why 1 DQS matches 8 DQ?
If x32, we use:
  32 DQS?
  1 DQS?
Actually, for DQS/DQ matching, it’s different one by one. Other types of applications may use different strobe- to-data ratios. For example, servers using x72 DIMMs based on x4 components require controllers with one strobe per four bits, and controllers for graphics or com- munications applications might use one to four strobes per 32 bits.

## Slide 35: RDQS/TDQS
For x4 and x8 mixed design.

## Slide 36: Why TDQS?
To simplify memory controller design for systems that simultaneously use both x4-based and x8-based registered DIMMs, DDR3 provides the termination data strobe (TDQS) function. DIMMs that are x8-based only require one DQ strobe pair (DQS/DQS#) for each 8-bit byte; x4-based DIMMs require a DQS pair for each 4-bit nibble (a total of four strobe lines). When these two different DIMM configurations are mixed within the same system, the loading of the DQS lines differs. These loading differences can cause signal integrity issues.
TDQS is similar to the RDQS function in DDR2, however, TDQS provides only termination. RDQS provides both termination and an output strobe.
Using the TDQS feature to reduce signal- integrity issues associated with mismatched DQS loading in combined x4-based/ x8-based systems.

## Slide 37: DQS-DQ Edge Aligned vs Center Aligned
For easy control of the delay circuit, which can be done only by controller.
  For READs, the data strobe signals are edge-aligned with the data signals, meaning that all data and data strobes are clocked out of the device by the same inter- nal clock signal, and all will transition at the outputs at nominally the same time. The controller will internally delay the received strobe to the center of the received data eye.
  For WRITEs, the controller must provide the data strobes center-aligned relative to data. That is, strobe transitions occur nominally 90 degrees (relative to the clock frequency) out of phase with data transitions. The DRAM device uses internally matched routing for the strobes and data such that the strobes can be used directly to capture input data. Note that the reason READs and WRITEs use a different alignment scheme is so that the delay circuitry can be centralized in one place (the controller) and does not have to be repli- cated in every DRAM device in the system. This ap- proach is expected to be carried forward to future gen- erations of DDR to leverage the infrastructure now be- ing established.
    Center Alignment creates the largest timing margin for the capture latches. Timing parameters, such as data setup (tS) and hold (tH).

## Slide 38: Why DQ not differential?
DQ is a data signal, and can tolerate more skew than DQS.

## Slide 39: Data Mask(DM)
Because dram burst length is often more than one byte, so, if we only write one byte(or less than the burst unit), the other bytes must be kept.
So, DM is a must.

## Slide 40: Reset Pin
/RESET pin is introduced in DDR3 for system stability.
It prevents and handle illegal commands and/or unwanted states.
Why reset pin is effective on low?
  Generally reset pin takes active low inputs . Main purpose of reset pin is to monitor the power fluctuations supplied to microcontroller . When ever power goes above / below threshold voltage reset circuitry triggers an active low signal on Reset pin.

## Slide 41: Synchronous Reset vs Asynchronous Reset
Synchronous reset means reset is sampled with respect to clock. In other words, when reset is enabled, it will not be effective till the next active clock edge.
In asynchronous reset, reset is sampled independent of clk. That means, when reset is enabled it will be effective immediately and will not check or wait for the clock edges.

## Slide 42: CPU Data Width == Dram Data Width?
Early PC, CPU Data Width is equal to dram data width.
Moden PC and moden phone don’t need they are equal.
  Moden transfer protocol can handle the mismatch of data width, eg: AXI.

## Slide 43: x4 x8 x16
Standard DRAMs support data-bus widths of 4 (x4), or 8 (x8), or 16 (x16) bits. Servers, cloud, and data-center applications use the x4 DRAMs as they allow a higher density on DIMMs, and enable RAS features that cut application downtime due to memory failures. The x8 and x16 DRAMs are less expensive and are commonly used in desktops and notebooks.
For x4:
  Page size is small, maybe 512B, it can reduce power of activate.

## Slide 44: The fullname of ZQ
ZQ calibration: calibration I/O impedance.
Impedance: aka as Z.
I/O: aka as Q.

## Slide 45: Why is ZQ resister 240 ohm?
For easy to set to 34, 40, 60ohm...

## Slide 46: Multi Channel
Multi channel can improve bandwidth because multi data transfer at the same time.
Multi channel means multi controller, every controller can work independently of each other.

## Slide 47: Where does Rank come from?
The term rank was created and defined by JEDEC, the memory industry standards group, to distinguish between the number of memory banks on a module.
Rank: (中文) 把…分等级; 属于某等级; 排列; 使排成行.

## Slide 48: Multi Rank
Increasing the number of ranks is mainly intended to increase the memory density per channel. Too many ranks in the channel can cause excessive loading and decrease the speed of the channel. Also some memory controllers have a maximum supported number of ranks.

## Slide 49: Where does Bank come from?
Multiple banks are provided so we can be simultaneously working on different requests.
Bank: (中文)银行; (尤指赌博中的) 筹码; 赌本; 库存; 库.

## Slide 50: Why 8 banks occurs in LP3/LP4?
2 banks or 4 banks exsit in early dram.
8 banks seems to be the best choice.
  For random memory accesses, i.e., to different rows, each bank can only be accessed once per tRC. Let us suppose that the data burst interval is 8ns (1000MT/s) and tRC is 56ns. Then only one-seventh of the nominal data transfer rate can be sustained by one bank.
Notes: http://www.qdpma.com/ServerSystems/DRAM.html

## Slide 51: Sense Amplifier/Row buffer
Sense Amplifier’s another name is “Row Buffer”.
Why need Sense Amplifier?
  Bit cells of SRAM are made very small to reduce the cost. Thus, turning bit-lines to logic 0 or 1 using small cells require much longer time.
  To solve these issues both bit-lines are precharged to Vdd (logic 1). A single cell is electrically connected to bit-lines for a small time to make a small difference in voltages. Later, the sense amplifier senses that difference and convert that small difference to logic 1 and logic 0.
  1T1C Structure : read from DRAM is destructive, so recover memory info is a must, sense amplifier occurs.

## Slide 52: Row buffers act as a cache within DRAM
Row buffer hit: only move data from row buffer to pins.
Empty row buffer access: must first read arrays, then move data from row buffer to pins.
Row buffer conflict: must first writeback the existing row, then read new row, then move data to pins.

## Slide 53: How to select Page Size?

## Slide 54: Prefetch
Prefetch is the term describing how many words of data are fetched every time a column command is performed with DDR memories.

## Slide 55: 2n prefetch for READ and WRITE

## Slide 56: Burst Length
Burst Length is often the multiple of prefetch size.
Burst Length should be equal or fraction of the size of cache line for better performance.
  LP4(x16):
    Prefetch Size: 16
    Burst Length: 16 or 32
    Cache Line(Arm(64)): 32 or 64 Bytes

## Slide 57: Burst Interleave
Burst Interleave is more efficient for some CPUs.

## Slide 58: Burst Terminate
DDR:

## Slide 59: Where does Bank Group come from?
Notes: https://books.google.com.hk/books?id=w9XBBAAAQBAJ&pg=PA87&lpg=PA87&dq=GDDR3+bank+group&source=bl&ots=otY1K8Ge8f&sig=ACfU3U13MPmgeUJffQiGqJxtn9mnrvaUZg&hl=en&sa=X&ved=2ahUKEwiOlu7Cu9znAhXPCuwKHRW-Bn4Q6AEwDnoECAoQAQ#v=onepage&q=GDDR3%20bank%20group&f=false

## Slide 60: Bank Group
The bank groups feature used in DDR4 SDRAMs was borrowed from the GDDR5 graphics memories.
DDR4 introduces the concept of Bank Groups that allows the system designer to build interleaved memory arrays down to the individual device level. For smaller systems which may have only a single memory device, this Bank Group feature can offer substantial benefits.
For example, one bank group can receive a series of pipelined commands for its upcoming data transfers. Once the first Bank Group starts its actual data transfers, another Bank Group can be initialized with its separate set of pipelined commands. After the first Bank Group completes its data transfers, the second Bank Group can initiate its data transfers, since it has already received its set of pipelined commands. In many cases, this Bank Group command pipelining can significantly reduce the impact of memory device delays, such as shown below.

## Slide 61: No Bank Group vs Bank Group

## Slide 62: tCCD_L vs tCCD_S

## Slide 63: Bank Interleave
Bank interleaving, which represents a significant advantage for applications accessing random data. Bank interleaving can be extremely effective for concurrent operations and can hide the timing overhead that is otherwise required for opening and closing individual banks.
  OFF: Banks are not interleaved, and address will be decoded as bank-row-column. ON: Banks are interleaved, and address will be decoded as row-bank-column.

## Slide 64: Advantage of bank interleave

## Slide 65: BC4
Due to the 8n-prefetch architecture of DDR3, one burst must be 8 bits. Burst chop 4 (BC4) mode uses internal control signals to select only the first 4 bits of data to read or write. So, the entire command excution time for BL8 and BC4 is the same. If you are using a valid data cycle and total clock cycle to calculate efficiency, BC4 has a very low efficiency (lower than 50%). For a large data transfer and high-bandwidth application, BC4 is not suitable.
The only real benefit to the burst chop mechanism is that it allows better data bus utilization in dual rank memory systems, where the rank switching overhead may be shorter than the (same rank) burst chop idle time.

## Slide 66: BC4 benifits in multi-rank system

## Slide 67: FSP
Easy and fast when switch from one freq to another freq.
Used in LPDDR4 and LPDDR5.
This rapid switching is enabled by the addition of frequency set points (FSPs). LPDDR4 specifies two FSPs, which are copies of all the DRAM registers that store operating parameters which might need to be changed for operation at two different frequencies. Once both operating frequencies are trained and the parameters stored in each of the two corresponding FSPs, switching between the frequencies can be accomplished by a single mode register write. This reduces the latency for frequency changes and enables the system to operate at the optimal speed for the workload more often.
“It supports end-user flexibility,” noted Vuong. “Some designers like to run their devices as fast as they can and then put them to sleep. Others like to run at lower frequencies – and lower power – when possible. A process might take a little longer but that’s a trade-off they’re willing to make. We designed LPDDR4 to be flexible enough to allow the end-user to decide what they want to do.” With that flexibility comes superior performance – an LPDDR4 device, at a similar data rate, will consume less power than an LPDDR3 device.

## Slide 68: DLL
DLL: Delay Locked Loop.
DDR3/DDR4 use DLL.
A DLL is used to maintain the timing relationship between a clock signal and an output data signal. A critical element of the DLL is the phase detector, which detects phase differences between the clock and output data.
LPDDR3/LPDDR4 don’t use DLL for low power.
  CK to DQS is not synchronized.
  How to fix the problem??

## Slide 69: Byte Mode(LP4)
JESD21-C
  LP4 x16  2 x 8

## Slide 70: Why Dram Freq 2667 not 2777?
From history, the base clock is 100M or 133M.
  Intel’s memory controller operates at either 100 or 133 MHz, producing multiples of 200 or 266.6MHz at integer ratios.
Dram freq is the multiple of the base clock.
  2667 == 133.3333 * 20.

## Slide 71: What’s the initialized data of DRAM?
Jedec Spec don’t specified the initialized data of dram, it’s meaningless.

## Slide 72: Dynamic ODT
Dynamic ODT allows a DDR3 SDRAM device to change termination values seamlessly between write commands issued to different modules. This feature is not available in DDR2 SDRAM systems, which require a bus idle time when changing termination values on the same device.
Dynamic ODT enables the DRAM to switch between high or low termination impedance without issuing a mode register set command. This is advantageous because it improves bus scheduling and decreases bus idle time.

## Slide 73: Switch between RTT_NOM RTT_WR

## Slide 74: ODT Park
PC4.
Improvements to the ODT protocol and a new Park Mode allow for a nominal termination and dynamic write termination without having to drive the ODT pin.
It’s often used in multi-rank system.

## Slide 75: Power Consumption of ODT

## Slide 76: Only one ODT of two ranks
Since the two ranks are physically very close on the memory, only one ODT signal is necessary for proper termination.
Non-Target ODT:
  LP5 introduce the new ODT Mode, which can improve signal integraty.

## Slide 77: ODT when power down
Users can define whether ODT can be on/off during PD with MR11 OP<2>. It is intended to offer easy ODT control with 2 rank configuration.
  LPDDR3.

## Slide 78: VDDQ Termination vs VSSQ Termination
LP4: VSSQ Termination;
  LVSTL
PC4: VDDQ Termination.
  POD12

## Slide 79: IO

## Slide 80: Dram Package

## Slide 81: A Die? B Die?
Different Types of Die.
Maybe 10nm, 20nm difference, or dram density, channel, rank...
A Die is better than B Die?
  No, just die type.

## Slide 82: DIMM
A DIMM or dual in-line memory module comprises a series of dynamic random-access memory integrated circuits. These modules are mounted on a printed circuit board and designed for use in personal computers, workstations and servers.
DIMM is used to assemble bigger data width and bigger density dram.

## Slide 83: The Types of DIMM
Unbuffered DIMMs (UDIMMs) -- Used mainly on desktop and laptop computers. Although they run faster and cost less, UDIMMs aren’t as stable as registered memory. Commands go directly from the memory controller residing in the CPU to the memory module.
Fully-buffered DIMMs (FB-DIMMs) – Usually used as main memory in systems that require large capacities, such as servers and workstations. FB-DIMMs use advanced memory buffer (AMB) chips to boost reliability, maintain signal integrity and improve methods to detect errors to reduce soft errors. The AMB bus is split into a 14-bit read bus and a 10-bit write bus. Having a dedicated read/write bus means reads and writes can happen at the same, which results in increased performance.
Registered DIMMs (RDIMMs) -- Also known as buffered memory, RDIMMs are often used in servers and other applications that require robustness and stability. RDIMMs feature onboard memory registers that are placed between the memory and the memory controller. The memory controller buffers command, addressing and clock cycling, and directs instructions to the dedicated memory registers rather than directly accessing the DRAM. Consequently, the instructions could take about one CPU cycle longer. However, the buffering reduces the strain on the CPU's memory controller.
Load-reduced DIMMs (LR-DIMMs) – Use isolation memory buffer (iMB) technology that buffers the data and address lanes, reducing the load on the memory controller. The iMB chip also buffers data signals, unlike the register on RDIMMs, which only buffers command, addressing and clock cycling. The iMB chip isolates all electrical loading, including data signals of the DRAM chips on the DIMM from the memory controller. As a result, the memory controller only sees the iMB and not the DRAM chips. The memory buffer then handles all the reads and writes to the DRAM chips, enhancing capacity and speed.
SO-DIMM -- While the standard DIMM is in the form of a rectangular stick approximately 5.5 inches in length, the small outline dual in-line memory module (SO-DIMM) is about half that size at 2.74 inches long. Both types of DIMMs are most commonly 1.2 inches tall, but both are made in a very low profile (VLP) format that is only 0.8 inches tall. SO-DIMM is mainly used for portable computing devices such as laptops and tablets. It differs from standard DIMM in that the DDR4 SO-DIMM has 260 pins versus 288 pins for the DRR4 DIMM. Standard DIMMs are used in PCs and servers. The VLP DIMM was developed to meet the space requirements of blade servers.

## Slide 84: SIP
SiP (System in Package) integrates multiple functional chips, including processors, memory and other functional chips, into one package. SiP technology is not just an integrated circuit package containing multiple chips. SiP chip is an integrated circuit with one or more different functions. It may contain passive components and/or MEMS and be assembled in a single standard package to form a system or subsystem. The advantage of SiP packaging technology is the ability to integrate multiple IC, packaging and testing technologies, creating highly integrated products with optimized cost, scale and performance.

## Slide 85: Lead-Free and RoHS
RoHS (Restriction of Hazardous Substances) is a European Union directive that restricts the use of lead, mercury, cadmium, chromium (VI), PBBs, and PBDEs in electrical and electronic equipment as of July 1, 2006.
Due to environmental concerns, the need for lead-free solutions in electronic components and systems is receiving increasing attention within the semiconductor and electronics industries. Maxim Integrated is committed to working with our customers to be able to offer products which meet their specific needs while complying with RoHS legislation.

## Slide 86: Dram State Diagram
A significant difference between the conventional DRAM and the SDRAM is the way in which memory access is executed. In a standard DRAM, the toggling of the external control inputs has a direct effect on the internal memory array. Whereas, in a SDRAM, the input signals are latched into a control logic block which functions as the input to a state machine. Therefore, the state machine actually controls the memory access.

## Slide 87: Dram Features

## Slide 88: Why dram needs training?
If layout is very good, the trace length and the length of all Pin’s layout are equal, dram signals are started and arrived at the same time, no need training.

## Slide 89: Drive Strength
DDR2: optional OCD.
DDR3: ZQ Calibration.

## Slide 90: Precharge

## Slide 91: Read/Write preamble/postamble
Dram Controller or DRAM needs to check it for correct read or write.
The preamble portion provides a timing window for the receiving device to enable its data capture circuitry while a known/valid level is present on the strobe sig- nal, thus avoiding false triggers of the capture circuit.

## Slide 92: Write Recovery
The time interval between the termination of a write pulse and the initiation of a new cycle, this time interval being provided for the memory to recover from a write operation and operate correctly.
  Write recovery time is the actual time interval between two signal events and is determined by the system in which the memory operates. A minimum value is specified that is the shortest interval for which correct operation of the memory is to be expected.
In highspeed SRAM, write recovery time is an important component of the write cycle time. It is defined as the time necessary to recover from the write cycle to the read state after the WE signal is disabled.

## Slide 93: tFAW
If the consecutive read operations are falling each time in a different ROW within each bank than you have the activation problem kicking in each time. In order to avert a high current drain from the arrays you need to limit the number of consecutive bank activation over a rolling window of time.

## Slide 94: Why 9 tREFI?
tRFC min = 350ns, tREFI min = 3.9us.
3.9us / 350ns = 11.
9?

## Slide 95: Loopback Mode
DDR5.

## Slide 96: Target Row Refresh
Row Hammer.
When a target row of a dynamic random access memory (DRAM) is activated too many times within a time period, the data stored at adjacent rows, which are physically adjacent to the target row, may be disturbed or lost. In particular, due to increasing density of DRAM design, the data stored at an adjacent row may be corrupted due to noise generated from the frequent activation of the target row.
Testing for TRR support: It should be possible to test whether a memory controller supports Target Row Refresh (TRR) and has it enabled. If TRR is enabled, then if we repeatedly activate two different rows, we should see a delay when the memory controller refreshes their four neighbouring rows.
LP4: MR24

## Slide 97: Read Mask
SDR SDRAM uses Read Mask, it‘s phased out after DDR SDRAM.

## Slide 98: MRR/MRS
PC4: MRS Commands can be issued only when DRAM is at idle state.
LP3:
  Idle/Active: can do MRR.
  Idle: can do MRW.

## Slide 99: Command Address Latency(CAL)
DDR4 also offers programmable Command-to-Address Latency that can be used to improve system power efficiency.

## Slide 100: Additive Latency
First appear on DDR2.
Additive latency allows a read or write command to be issued immediately following the active command.
Allows ACTIVATE – READ/WRITE to be done together.

## Slide 101: Read Leveling
DQ-DQS delay.
PC3:
  Read leveling is a specification that adjusts the output skew from each DRAM on the controller side. Since DDR3 operates at high speed, correct data input may not be possible without timing adjustment.
  In addition to the memory array, a ROM that retains specific data patterns is provided. The MPR function intended to assist the read leveling outputs data from the ROM.
  The specific data patterns enable timing adjustment during READ operation. Note: To use MPR, the controller side must be compatible with MPR.

## Slide 102: Write Leveling

## Slide 103: Burst Interrupt
An efficient pipeline of multiple column reads is already possible by simply sending multiple read commands spaced as closely as the desired burst length dictates.
https://en.wikipedia.org/wiki/Synchronous_dynamic_random-access_memory#Interrupting_a_read_burst

## Slide 104: ECC
DDR5/LPDDR5 support ECC.

## Slide 105: Deep Sleep Mode
LPDDR5: DSM Mode.

## Slide 106: Write X
LP5.

## Slide 107: DVFS
LP5:

## Slide 108: WCK
LP5:

## Slide 109: Clock Stop Mode
The clock can be stopped if no DRAM operations are in progress that would be affected by this change. Any DRAM operation already in process must be completed before entering clock stop mode.
This feature increases power savings by having fewer transitions on the clock path. There are predominantly two methods used to achieve this according to Micron Technology:
  Changing the clock frequency when the data transfers require a different rate of speed, or,
  Holding CKE HIGH, with CK LOW and CK HIGH for the full duration of Clock Stop Mode
The method being used is based on an individual product’s requirements. Mobile DDR memory can change the clock frequency during operation, but this is only allowed when all the timing and memory refreshing requirements are met.
According to JEDEC, the clock can even be stopped completely under the following conditions:
  The last command (ACTIVE, READ, WRITE, PRECHARGE, AUTO REFRESH or MODE REGISTER SET) has executed to completion, including any data-out during read bursts; the number of clock pulses per access command depends on the device’s AC timing parameters and the clock frequency.
  The related timing conditions (tRCD, tWR, tRP, tRFC, tMRD) have been met.
  CKE is held High.

## Slide 110: Clock Stop Mode(Cont.)
PC3:
  The input clock frequency can be changed from one stable clock rate to another stable clock rate under two conditions: (1) Self-Refresh mode and (2) Precharge Power-down mode. Outside of these two modes, it is illegal to change the clock frequency.

## Slide 111: Test Mode
PC3:
  The normal operating mode is selected by MR0 (bit A7 = 0) and all other bits set to the desired values shown in Figure 2.3.2. Programming bit A7 to a ‘1’ places the DDR3 SDRAM into a test mode that is only used by the DRAM Manufacturer and should NOT be used. No operations or functionality is specified if A7 = 1.

## Slide 112: Connectivity Test Mode
Aka as “Boundary Scan Test”.
PC4: TEN pin.
JEDEC organization has defined Connectivity Test Mode for DDR4 memories in order to speed up testing of electrical continuity of pin interconnection between host device and memory.
  DDR4 Connectivity tester perform an exhaustive test covering data and address buses as well as memory control signals following the JEDEC standard.
  The comprehensive set of test patterns guarantees detection of static defects (shorts, opens, bridging faults) on memory interconnection lines.
  Memory controller can test and detect connectivity faults without needing to go through DRAM initialization sequencing.

## Slide 113: Uncontrolled Power Off
At most 400 times?

## Slide 114: Per DRAM Addressability

## Slide 115: Gear Down Mode
A Reliability, Availability and Serviceability (aka RAS) feature more clearly documented in the new JEDEC DDR4 Rev B spec, Gear-down mode, allows the DRAM Address/Command and Control bus to use every other rising clock of the DDR4 Memory bus clock.

## Slide 116: Write CRC
CRC error detection provides real-time error detection on the DDR4 data bus, improv- ing system reliability during WRITE operations. DDR4 uses an 8-bit CRC header error control: X8+X2+X+1 (ATM-8 HEC).

## Slide 117: Command/Address Parity
PC4:
  [A2:A0] of MR5 are defined to enable or disable C/A Parity in the DRAM. The default state of the C/A Parity bits is disabled.

## Slide 118: Multi Purpose Register
(Aka) MPR, First appear on PC3.
Multipurpose register (MPR) function, MPR Access Mode, is used to write/read specialized data to/from the DRAM.
During Read Leveling the memory controller adjusts for the delays introduced by the fly-by memory topology that impact the read cycle. This is done via the addition of a special Multi-Purpose Register (MPR) in the DDR3 memory device. The MPR can be loaded with predefined data values via a special command from the memory controller. These data values can be used for system timing calibration by the memory controller.
As shown in Figure below, the MPR can be selected, by setting a bit in another memory register (EMRS3, bit A2), to switch the source of data for memory read to come from the MPR, not the normal memory array. The MPR data is substituted for the DQ, DM, DQS and /DQS pads on the memory device. This feature allows the memory controller to calibrate the timing of the read path to adjust for any additional delays introduced by the DDR3 fly-by architecture.

## Slide 119: Multi Purpose Register(Cont.)

## Slide 120: All Bank Refresh vs Per Bank Refresh

## Slide 121: PASR
Partitial Array Self Refresh.

## Slide 122: TCSR
Mobile DDR SDRAM incorporates several low power functionalities
into DDR SDRAM to reduce the standby current. First, the supply voltage is
reduced to 1.8V from 2.5V, providing half of the power reduction. Second, it
now can support partial array self refresh (P ASR), only half or one-fourth,
instead of whole DRAM array. Thus, only the array with the valid data will
be refreshed to avoid unnecessary self refresh current. To further reduce the
self refresh current, it also lengthens the refresh period for lower temperature, called temperature compensated self refresh (TCSR). Finally, when the DRAM is not used, e.g., the standby mode in the mobile devices, these low power DRAMs can enter into the deep power down mode to completely turn off the self-refresh operation.

## Slide 123: ASR SRT
Auto Self Refresh & Self Refresh Temperature.
If the normal case temperature limit of 85°C is not exceeded, then neither SRT nor ASR is required, and both can be disabled throughout operation. However, if the extended temperature option of 95°C is needed, the user is required to provide a 2x refresh rate during (manual) refresh and to enable either the SRT or the ASR to ensure self refresh is performed at the 2x rate.
SRT forces the DRAM to switch the internal self refresh rate from 1x to 2x. Self refresh is performed at the 2x refresh rate regardless of the case temperature.
ASR automatically switches the DRAM’s internal self refresh rate from 1x to 2x. Howev- er, while in self refresh mode, ASR enables the refresh rate to automatically adjust be- tween 1x to 2x over the supported temperature range. One other disadvantage with ASR is the DRAM cannot always switch from a 1x to a 2x refresh rate at an exact case temper- ature of 85°C. Although the DRAM will support data integrity when it switches from a 1x to a 2x refresh rate, it may switch at a lower temperature than 85°C.
Since only one mode is necessary, SRT and ASR cannot be enabled at the same time.
DDR3: optional.

## Slide 124: Fine Granularity Refresh
First appear on PC4.
The accurate refresh mode: 1x/2x/4x..

## Slide 125: Self Refresh Abort
PC4/LP4.
Why self refresh abort?
  During internal DRAM memory refreshes, the memory controller has no visibility to when this refresh is initiated. As a result, the controller is designed to wait for an entire refresh cycle (tRFC, plus a guard band, e.g., 10 ns) before issuing a command to the DRAM. The time period a memory controller must wait before issuing a valid command is herein referred to as tXS (i.e., tRFC+10 ns). tRFC for a 2 Gbit device is in the range of 160 ns. The tRFC approximately doubles as DRAM devices increase in density (e.g., tRFC for a 4 GBit device is in the range of 300 ns, tRFC for an 8 Gbit device is in the range of 550 ns), thus increasing tXS.
  Therefore it is desirable to reduce the value of tXS for DRAM devices in order to reduce the time a memory controller must wait before issuing valid commands.

## Slide 126: Fly-By Topology
DDR3 uses fly-by topology for CMD/ADD/CLK signals to improve signal quality.This causes flight time difference between DQ/DM/DQS and CMD/ADD/CLK. DDR3 has de-skew mechanism to compensate flight time difference.

## Slide 127: DBI
Data bus inversion (DBI) to help improve signal integrity while reducing power consumption, but it increases read or write latency.
Why DDR4/LPDDR4 supports DBI, DDR3/LPDDR3 don’t support?

## Slide 128: Power Down Mode
Power Down Mode - can modestly save system power at the expense of higher DRAM latency by putting DRAM into a quiescent state after a period of inactivity.
Power Down and Self Refresh are 2 low power states of DRAM devices. One of the primary differences between these states is that in the Self Refresh state, the DRAM executes internal refreshes which allows the memory controller and PHY to be disabled for a long time. In the power down state, the DRAM still requires refresh commands to be sent to maintain the memory contents.
LP4: Entering power-down deactivates the input and output buffers, excluding CKE and RESET.
Maximum power-down duration is governed by the refresh requirements of the device.

## Slide 129: DPD(Deep Power Down)
LP3
PC4: MR4 A4
The JEDEC standard specifies a Deep Power-Down (DPD) mode, in which the entire memory array shuts down. All internal voltage generators inside the device stop and all data is lost, as is all the information in the Mode Register Set (MRS) and the EMRS.

## Slide 130: IDD
What’s IDD?
  The current draw from the VDD terminal of the device (the IDD).

## Slide 131: Illegal operation or timing
LP3: Operation or timing that is not specified is illegal, and after such an event, in order to guarantee proper operation, the LPDDR3 device must be powered down and then restarted through the specified initialization sequence before normal operation can continue.

## Slide 132: AXI
AXI to DRAM

## Slide 133: Cache Line

## Slide 134: Bit Flip will cause crash?
Maybe, maybe not.
Consider that many data file, eg: audio, movie, text file, if one bit flip occurs, the instructions are normal, so the system may be work normally!

## Slide 135: Reference
Google Search.
Wiki.